## Slide 1
ESP32 · WiFi · RSSI · UAV
Drone-Based
Crowd Monitoring
Using ESP32 WiFi Sniffing for Localization & Density Estimation
Real-Time RF-Based Indoor Positioning System
Mohit Patil 23BRS1185

## Slide 2
Objective
📡
Passive Detection
Detect nearby WiFi-enabled devices using promiscuous packet sniffing — no active connection needed.
📍
RSSI Localization
Estimate device positions using Received Signal Strength Indicator (RSSI) from multiple ESP32 nodes.
🗺️
Real-Time Density Map
Visualize crowd concentration on a live GUI, enabling actionable situational awareness.

## Slide 3
System Architecture
WiFi
Devices
▶
ESP32
Nodes
▶
Backend
Server
▶
Trilater-
ation
▶
GUI
Display
Phones, laptops emit probe requests
Capture packets in promiscuous mode
Aggregate RSSI from all nodes
Compute (x,y) coordinates
Plot density heatmap live

## Slide 4
ESP32 WiFi Sniffing
How It Works
ESP32 set to promiscuous mode
Intercepts 802.11 management frames
Extracts source MAC address per packet
Records RSSI (signal strength in dBm)
Sends data via TCP/UDP to server
No user association or authentication needed
Packet Callback (Pseudocode)
void sniffer_cb(
wifi_promiscuous_pkt_t *pkt) {
int8_t rssi =
pkt->rx_ctrl.rssi;
uint8_t *mac =
pkt->payload[10];
send_to_server(mac, rssi);
}

## Slide 5
RSSI → Distance: The Math
Log-Distance Path Loss Model
RSSI(d) = RSSI₀ − 10 · n · log₁₀(d / d₀)
Solving for Distance d:
d = d₀ · 10^((RSSI₀ − RSSI) / (10 · n))
RSSI₀
Reference RSSI at d₀=1m (typically −40 to −55 dBm)
n
Path loss exponent (free space ≈ 2, indoor ≈ 2.7–3.5)
d
Estimated distance from ESP32 node to device (metres)
RSSI
Measured signal strength from captured packet (dBm)

## Slide 6
Trilateration: Position Calculation
Circle Equations from 3 Nodes
Node 1:
(x−x₁)² + (y−y₁)² = r₁²
Node 2:
(x−x₂)² + (y−y₂)² = r₂²
Node 3:
(x−x₃)² + (y−y₃)² = r₃²
Linearised (subtract eq₃ from eq₁, eq₂):
Ax = b → x = (AᵀA)⁻¹Aᵀb
Geometric Intersection
N₁
N₂
N₃
(x,y)

## Slide 7
Least-Squares Position Solver
Matrix Form — Subtracting the last equation eliminates nonlinear terms:
2(xᵢ−xₙ)·x + 2(yᵢ−yₙ)·y = rₙ²−rᵢ² + xᵢ²−xₙ² + yᵢ²−yₙ²
A =
⎡ 2(x₁−x₃) 2(y₁−y₃) ⎤
⎣ 2(x₂−x₃) 2(y₂−y₃) ⎦
b =
⎡ r₃²−r₁² + x₁²−x₃² + y₁²−y₃² ⎤
⎣ r₃²−r₂² + x₂²−x₃² + y₂²−y₃² ⎦
Solution:
x̂ = (AᵀA)⁻¹Aᵀb
→ [x, y]ᵀ
⚠ RSSI noise adds uncertainty to rᵢ → Weighted Least Squares (WLS) assigns higher weight to stronger (closer) signals for better accuracy.

## Slide 8
Backend Processing Pipeline
01
Packet Ingestion
ESP32 nodes stream (MAC, RSSI, node_id, timestamp) tuples over UDP to the backend server.
02
MAC Grouping
Buffer groups packets by MAC address. Waits for readings from ≥3 nodes within a 500 ms window.
03
Distance Estimation
Apply RSSI→distance formula per node. Convert raw dBm to metres using calibrated RSSI₀ and n.
04
Trilateration Solve
Construct A and b matrices. Solve x̂=(AᵀA)⁻¹Aᵀb. Output (x,y) position in the floor-plan coordinate frame.

## Slide 9
Real-Time GUI Visualization
Display Features
🔴 Red dots = detected devices
📐 (x, y) coordinate labels
🔄 Live refresh every 500 ms
🌡️ Heatmap density overlay
📏 Scalable floor-plan canvas
🔗 WebSocket / REST data feed
Floor-Plan View (Mock)
N1
N2
N3
(3.2, 4.7)

## Slide 10
Applications
👥
Crowd Monitoring
Track crowd density at concerts, stadiums, and public events. Enable proactive safety responses.
🚨
Disaster Management
Locate survivors in collapsed structures by detecting their devices via passive RF sensing.
🏙️
Smart City Analytics
Generate pedestrian flow heatmaps to optimise city infrastructure and traffic management.
🎪
Event Management
Monitor real-time attendance, queue lengths, and bottleneck areas within event venues.

## Slide 11
Challenges & Mitigations
⚠ RSSI Noise & Multipath
Walls, furniture, and reflections cause RSSI to fluctuate by ±10 dBm, inflating distance errors.
✅ Mitigation
Kalman filter smoothing + Weighted Least Squares (weights ∝ 1/σ²) down-weight noisy readings.
⚠ MAC Address Randomisation
Modern iOS & Android randomise MAC per probe request, causing identity fragmentation.
✅ Mitigation
Cluster probe bursts within 100 ms windows; use sequence-number continuity as a soft identifier.
⚠ ESP32 Hardware Limits
Single-core sniffing + TCP send can miss packets at high packet rates (>500 pps).
✅ Mitigation
Use FreeRTOS dual-core: Core 0 sniffs, Core 1 processes & sends. Ring-buffer between cores.

## Slide 12
System Advantages
💰
Low-Cost Hardware
ESP32 module: ~₹300–500 each. Entire 3-node setup under ₹2,000 — orders of magnitude cheaper than camera systems.
🔒
Privacy-Preserving
No video capture. Only anonymised MAC hashes and RSSI values are processed — GDPR/PDPA friendly by design.
📷
No Camera Required
Works in darkness, smoke, or fog. Robust where optical sensors fail completely.
🚁
Drone-Portable
The entire sensor cluster weighs <200 g. Mount on a UAV for aerial, mobile crowd surveying.
📡
Passive & Covert
No RF emissions. The system only listens — undetectable to the devices being monitored.
⚡
Real-Time Output
Sub-second latency from packet capture to GUI update. Suitable for dynamic crowd management.

## Slide 13
Conclusion
A Scalable RF-Based
Crowd Intelligence System
Real-time crowd sensing using passive 802.11 sniffing — no cameras, no active probing.
Mathematically grounded position estimation via Least-Squares Trilateration.
Privacy-preserving, low-cost, and drone-deployable for dynamic environments.
Future Scope: Neural-network RSSI calibration · Drone swarm trilateration · Live heatmap streaming
Drone-Based Crowd Monitoring System | ESP32 WiFi Sniffing | RSSI Trilateration